## Slide 1: Bastion secure processor architecture
Ruby B. Lee
Princeton University

## Slide 2: Bastion’s Goals
Protect security-critical software modules within an untrusted software stack
  O.S. as a potential adversary
  Physical attacks in addition to software attacks
Set up secure compartments for trusted code, rather than sandbox for untrusted code
  Secure setup, execution and termination
Resilient execution of security-critical tasks even in the presence of malware and (unrelated) corrupted code in software stack
Enable scalability to multiple mutually suspicious trust domains
Provide a mechanism for reporting trust evidence

## Slide 3: Bastion: secure processor-hypervisor architecture
D. Champagne, R.B. Lee, "Scalable Architectural Support for Trusted Software",
IEEE Intl. Symp. on High-Performance Computer Architecture (HPCA), Jan. 2010
Notes: Secure compartments for trusted code and data rather than sandboxes for untrusted code
End with threat model: CPU chip is trusted
  successful internal probe is hard
All other hardware is untrusted
  memory chips, external buses, hard drives, etc.
Hypervisor and small Trusted Software Modules are trusted
All other software (OS and applications) is untrusted

## Slide 4: Bastion’s Trusted Software Modules
Each TSM has a security segment, module_ID & identity
Securely launched by new SECURE_LAUNCH hypercall
  Assigns module_id
  Computes module identity
    Hash of code & static data, and Hash of security segment
  Sets up module memory protection
Security segment

## Slide 5: Bastion Virtual Memory Mappings (SW attacks)
Set up by hypervisor during SECURE_LAUNCH hypercall
Hypervisor provides data to CPU on TLB miss
module_id zero reserved for untrusted software

## Slide 6: Secure Physical Memory (HW attacks)
hash_tree_root register

## Slide 7: Scalable Secure Storage (SS) sealed to each Trusted Software Module or Hypervisor
Notes: Talk about how you only need one set of (Hash, Key) registers to protect the hyperviser, but then thru the hyperviser’s SSA you can protect arbitrary number of SSAs for arbitrary number of TSMs.

## Slide 8: Minimal Layer-skipping Trust Chains
Provide firm anchor (in hardware) for Trust Chains
  Prevents “attacks from below”
Enable Minimal trust chains for integrity
Today: Full trust chain Tomorrow: Minimal trust chain
Enable trusted application execution -- even with a compromised OS and/or malware in an untrusted SW stack
  Enabling technology: SP or Bastion architecture
Notes: How to level the playing field for Cyber Security?
Allow security-critical execution even in the presence of malware

## Slide 9: Layer-skipping Integrity Checking
Notes: hardware can
    measure every layer of software, then that software measures other parts of system, or
    directly measure only trusted software in question

## Slide 10: Attestation of Remote System
Customers need attestation that
    correct code is executing on good platform
    untrusted subjects have not attempted to compromise the platform, code or data
    customer has secure means to connect to the remote code and data

## Slide 11: Bastion’s Tailored Attestation

## Slide 12: Bastion Architectural Concepts
Bastion architecture is a co-designed Processor-Hypervisor Trusted Computing Base (TCB)
Minimal, layer-skipping trust chain with HW trust anchors
  Processor hardware protects Hypervisor
  Hypervisor protects Trusted Software Modules
Runtime Protection
  Shadow access control for enhanced virtual-to-physical memory mappings (protection from SW attacks)
  physical memory authentication (protection from HW attacks)
  Secure inter-module control flow
Secure storage sealed to trusted module
  Scalability with hypervisor-protected “soft” registers for module-specific trust anchors
  Only 2 hardware trust anchors required
Efficient Processor-based Tailored Attestation
  Measurement of SW identities at Secure Launch
  Runtime protection and Reporting of Trust Evidence with Attest instruction

## Slide 13: New Security Mechanisms
Protecting the different phases of security-critical software

## Slide 14: Bastion: security mechanisms
Hypervisor Protection
  Secure Launch of Hypervisor
  Protecting Hypervisor at Runtime
Trusted Software Module Protection
  Secure Launch
  Secure Virtual-to-Physical Memory Mapping
  Secure Physical Memory
  Secure Inter-Module Control Flow
Trusted Computing Primitives
  Tailored Attestation
  Secure Storage
    sealed to each Trusted Software Module

## Slide 15: Instructions needed
Because of trusted software layer above the hardware, the hypervisor, Bastion only needs 2 new instructions:
  Hyperviser secure launch
  Attest hypervisor
Rest can be done with software Hypercalls.

## Slide 16: Bastion Supports Flexible Trust Domains

## Slide 17: Summary: Bastion Security
Hardware-protected hypervisor
Fine-grained module isolation and sharing
  Can provide Secure Execution Environments for Trusted Software Modules in App and OS spaces
Authenticated module transitions
Resilient attestation
Secure Memory
Module-specific secure storage

## Slide 18: Extras

## Slide 19: Beyond SP and TPM
How to scale SP to support multiple simultaneous Trusted Software Modules (TSM) from different trust-domains?
What best security functions provided by TPM can be built into microprocessor? How?
Enable resilient execution of security-critical tasks
  Provide resilient attestation

## Slide 20: Extending SP: Design Goals
Provide application-level security without trust in OS (SP philosophy)
Extend the SP architecture to support multiple TSMs (main thrust)
Support full-blown memory integrity
Offer each TSM a piece of secure storage
Multiple TSM support means we need to:
  identify TSMs at launch
  distinguish between TSMs at runtime
  manage multiple contexts
  provide remote attestation

## Slide 21: The Hypervisor as a “Super TSM”
Managing multiple secure contexts in hardware is hard
  Hardware has poor visibility into software contexts
  Very limited on-chip storage
  Complex, “software-type” management functionalities required
A thin hypervisor is great as a secure context manager:
  Fits in a few thousand lines of code
  Decent visibility into software context
  Quasi-unlimited secure storage
  Can easily handle whole range of critical tasks
    TSM launch
    runtime identification
    secure context switch
    etc…

## Slide 22: Secure Module Transitions
Asynchronous transitions:
  Triggered by: module preemption/resumption
  Hypervisor action: save/restore module registers
Synchronous transitions:
  Triggered by: call_module/return_module instructions
  Hypervisor action: check call/return sequence, authenticate caller/callee

## Slide 23: Conclusions
Bastion TCB provides Tailored Attestation: resilient, functional attestation
This is enabled by TCB mechanisms providing core security functions:
Hardware-protected hypervisor
Fine-grain module isolation and sharing
Authenticated module transitions
Module-specific secure storage
An implementation on OpenSPARC demonstrates feasibility and improved performance over TPM attestation and secure storage